## Slide 1: Missing Image Detection in Melt Pool Monitoring
Vikranth Gadi & Athul C. D
Team DELP, Purdue University
August 25
Washington, D.C.

## Slide 2: Contents
Exploratory Data Analysis
Dataset Generation
Part 1 Methodology
  Approach #1: Comparative Difference Analysis
  Approach #2: Similarity Metric Analysis
  Approach #3: Principal Component Analysis
  Results
Part 2 Methodology
  Approach #1: Artefact Detection and Velocity Estimation
  Approach #2: Shape Transformation
  Results
Conclusion

## Slide 3: Exploratory Data Analysis
Temporal evolution of the melt pool
Elliptical globe with a tail of fumes
Direction of fumes change continuously
Artefacts fly off occasionally
Sample data
Sample data with filtering
Part 2 data

## Slide 4: Image Thresholding
Values of pixels below threshold, set to 0; above to 255
  lambda p: 255 if p > threshold, else 0
Reduces noise and decreases dimension
Can remove artifacts
Threshold value: hyper parameter for methods!
Original
Threshold = 100
Threshold = 150
Threshold = 200

## Slide 5: Dataset Generation
Overall data pool (637 frames):
  Sample data (437 frames)
  Problem #1 data (first 200 frames)
Testing and Validation Split: 2% holdout
Five-fold Cross Validation
Criteria #2 for scoring
Frames synthetically removed to create dataset

## Slide 6: Difference between Frames
Difference between consecutive frames
Hypothesis: Missing frame will only be marginally different from the previous frame
In+1
In
Notes: WHich figures is the diff between

## Slide 7: Comparative Difference Analysis
Missing frame 63 corresponds to minima
Compute difference between missing frames and given frames
Minimize area of the difference
Area: Count of white pixels
Direct difference: In- Ix
Midpoint difference : 0.5(In+In+1)- Ix
Absolute difference: |In- Ix|+|In+1- Ix |
Missing Frame
Area after Direct Difference
Area
Frame number

## Slide 8: Center of Mass (COM)
Oscillates between different positions
Change is discrete; accompanied by tail flipping
Label and partition the dataset based on COM position
Measure COM of missing image and match to possible partitions
Evolution of y COM
Y Position
y COM
Frame number

## Slide 9: Similarity Comparison
Metrics
  Hamming distance
  Area of white pixels
    Count of white pixels
  SSIM (Structural Similarity Index Measure)
  PSNR (Peak Signal-to-Noise Ratio)
  NCC (Normalized cross correlation)
Missing Frame
Notes: Techniques used in image compression

## Slide 10: Challenges
Outliers: Empty frames and super-bright frames
Phenomenon is periodic; Missing frame can have multiple matches
Missing Frame
Area after Direct Difference
Frame number
Area

## Slide 11: Principal Component Analysis
Principal Component Analysis (PCA) is applied to detect frame skipping and analyze the temporal evolution of the laser melt pool process.
  Flatten each image into a 1D array
  Sudden jumps or discontinuities in PC values may indicate frame skips
  Different PCs may capture various aspects of the melt pool dynamics

## Slide 12: Results
Method |  | Average Score using Criteria #2
Random Sampling |  | 17.5
Comparative Difference Analysis | Direct Difference | 33.9
 | Midpoint | 36.1
 | Absolute Difference | 28.6
Similarity Analysis | Hamming Distance | 23.8
 | Area of White Pixels | 24.6
 | Structural Similarity Index Measure | 21.4
 | Peak Signal-to-Noise Ratio | 27.7
 | Normalized cross correlation | 29.8
Principal Component Analysis |  | 19.1

## Slide 13: Problem 2: Approach #1
Observations:
  Melt pool can be abstracted as a circle and approximated to an ellipse when viewed by a camera
  The plume can be abstracted as a parabola
Hypothesis: frame skipping will result in abrupt morphing of melt pool and plume shapes and tracking them for consistency can help detect existence of missing frames.
Schematic of selective laser melting and the heat transfer in molten pool. [1]
[1] Tan, C. et al. (2018) ‘Selective laser melting of high-performance pure tungsten: parameter design, densification behavior and mechanical properties’, Science and Technology of Advanced Materials, 19(1), pp. 370–380. doi: 10.1080/14686996.2018.1455154.

## Slide 14: Melt Pool and Plume Tracking
Key steps:
  Image preprocessing using binary thresholding
  Contour detection using Suzuki-Abe algorithm [1]
  Identification of optimal ellipse parameters using least square fitting
  Visualization of area change
[1] Suzuki, Satoshi. "Topological structural analysis of digitized binary images by border following." Computer vision, graphics, and image processing 30.1 (1985): 32-46.

## Slide 15: Problem 2: Approach #2
Observation: several artefacts appear sometimes which travel from the plume towards the edge in the region of interest
Hypothesis: frame skipping will result in abrupt changes in artefact position and tracking them can help detect existence of missing frames.
Schematic of artefacts generated in the process of selective laser melting. [1]
[1] Panwisawas C, Tang YT, Reed RC. Metal 3D printing as a disruptive technology for superalloys. Nat Commun. 2020 May 11;11(1):2327. doi: 10.1038/s41467-020-16188-7. PMID: 32393778; PMCID: PMC7214413.
Artefacts generated

## Slide 16: Artefact Detection and Tracking
+
+
+
+
+
+
Key steps:
  Preprocessing using binary thresholding
  Region of Interest (ROI) creation excludes main melt pool and plume areas
  Contour detection in ROI using Suzuki-Abe algorithm
  Artifact candidate filtering based on size and shape eliminates noise and non-artifact objects
  Temporal tracking for frame skip detection

## Slide 17: Results
Method | Average Score using Criteria #2
Random Sampling | 17.5
Principal Component Analysis | 19.1
Melt Pool and Plume Tracking | 20.6
Artefact Detection and Tracking | 18.3
Melt Pool, Plume and Artefact Tracking | 24.8

## Slide 18: Conclusion
Explored multiple approaches for detecting missing images in melt pool monitoring
  Simple difference-based methods outperformed more complex similarity measures for problem 1
  Combination of melt pool, plume, and artefact tracking is the best performing method for problem 2
Limited dataset size may impact generalizability
Given more time:
  Adaptive thresholding for varying lighting conditions
  Synthetic data generation using multi-physics simulation

## Slide 19: Thank You
Questions?